Data Transfer of Field-to-Finish Codes from SurvCadd to the SurvCE data collector.

In SurvCadd, we use an “fld” file to conduct field-to-finish.  Here is a simple one, below:

This file, MI3.fld, can be loaded in to the Field Code file format of SurvCE as follows.  Set SurvCE to File, Data Transfer, “Carlson Transfer”.  It will stay then in the File Transfer screen and “wait” on the PC.  Now back in SurvCadd, go to Tools, Data Collectors, SurvCE/Fast Survey/G2.  If you are cabled up correctly (and not in Active Sync mode), you will hook up instantly and see the following screen:

Here you select F2F conv, down in the lower right.  When you pick that option, you get prompted specifically for the fld file to select:

Then the file shows up on SurvCE in the c:\systemcf\data directory or whatever directory you specified.  To see the file, go to Feature Code List under File and load it.  Layer names, 3D vs 2D polyline aspects and exact code names are captured.