Update Topcon GPS Firmware & OAFs

- Robert Clayton 1-800-443-4567 helped out with this and supplied OAF that enabled ADU (for heading operation mode) parameter and Ben & Bryan 1-925-460-1333 helped with firmware updates. 1-866-4topcon – tech. support

- To update firmware you will need the following information before going to the website:

  - Board type using PC-CDU under Help/About to see this setting on the receiver

    - Odyssey-E: E_GGD_2

    - Hi-Per: HE_GD_3

- Go to the website:  topcongps.com and navigate to   /software and download the following if needed:

  - Under /utilities: FLoader   (firmware loader program)

  - When prompted for User ID: icecube     Password: hello!

  - Under /firmware select the necessary files for download.  They will be zipped, so unzip them before running FLoader.  You will need to do at least 2 different loads inside FLoader: one for “power board” file and then for the two “main” files “.ldp” & “.ldr”  These can be accessed by choosing the Device tab, and changing the Device Type to: Receiver’s Power Board and Receiver respectively then choosing the Program tab to select the necessary files and to perform the load.

- To update OAFs, you will need to send the following information to options@topconps.com (Better way now – see d):

  - Machine ID:

    - Odyssey-E ID: AFICJXVLBEO

    - Hi-Per ID: 8QY53N7D8N4

  - Serial:

    - Odyssey-E: PP0011

    - Hi-Per:

  - Sometimes they will ask you to send a copy of what you already have activated.  This can be found through PC-CDU under Tools/Receiver Options

  - http://www.topconps.com/options/optionmanager.cgi, use customer for the id & password.  Enter in the receiver ID then search, eg. MT300133500; but, usually shorter.  Information will come up on current configuration.  If using it for testing, make sure to indicate this in special comments section and check any needed items.  If using a dual antenna system, you will need to make sure ADU is selected.  Make sure you check the email address to see that yours is on the list.

- Once you receive OAF from Topcon – load it by using PC-CDU under Tools/Receiver Options and then Load.  Choose Soft Break Capture.  You will need separate OAF for each receiver, because it is ID specific.

- ADU used to need to be activated on both moving base and rover, but with firmware version 2.3p2 only needs to be active on rover.